Supplemental Data Item #2: U-Pb Geochronological Methodology

Detrital zircon crystals are extracted from samples by traditional methods of crushing and grinding, followed by separation with a Wilfley table, heavy liquids, and a Frantz magnetic separator. Samples are processed such that all zircons are retained in the final heavy mineral fraction. A large split of the zircon grains (generally thousands of grains) is incorporated into a one-inch epoxy mount together with fragments of Sri Lanka standard zircon (of known age).  The mounts are sanded down to depths of ~20 microns, polished, imaged, and cleaned prior to isotopic analysis.

U-Pb geochronology of zircons is conducted by laser ablation multicollector inductively coupled plasma mass spectrometry (LA-MC-ICPMS) at the Arizona LaserChron Center (Gehrels et al., 2006, 2008). The analyses involve ablation of zircon with a Photon Machines Analyte G2 excimer laser using a beam diameter of 30 microns. The ablated material is carried in helium into the plasma source of a Nu HR ICPMS, which is equipped with a flight tube of sufficient width that U, Th, and Pb isotopes are measured simultaneously. All measurements are made in static mode, using Faraday detectors with 3x1011 ohm resistors for 238U, 232Th, 208Pb-206Pb, and discrete dynode ion counters for 204Pb and 202Hg. Ion yields are ~0.8 mv per ppm. Each analysis consists of one 15-second integration on peaks with the laser off (for backgrounds), 15 one-second integrations with the laser firing, and a 30 second delay to purge the previous sample and prepare for the next analysis. The ablation pits are ~15 microns in depth.

For each analysis, the errors in determining 206Pb/238U and 206Pb/204Pb result in a measurement error of ~1-2% (at 2-sigma level) in the 206Pb/238U age. The errors in measurement of 206Pb/207Pb and 206Pb/204Pb also result in ~1-2% (at 2-sigma level) uncertainty in age for grains that are >1.0 Ga, but are substantially larger for younger grains due to low intensity of the 207Pb signal.For most analyses, the cross-over in precision of 206Pb/238U and 206Pb/207Pb ages occurs at ~1.0 Ga.

204Hg interference with 204Pb is accounted for by measurement of 202Hg during laser ablation and subtraction of 204Hg according to the natural 202Hg/204Hg of 4.35. This Hg correction is not significant for most analyses because our Hg backgrounds are low (generally ~300 cps at mass 204).

Common Pb correction is accomplished by using the Hg-corrected 204Pb and assuming an initial Pb composition from Stacey and Kramers (1975). Uncertainties of 1.5 for 206Pb/204Pb and 0.3 for 207Pb/204Pb are applied to these compositional values based on the variation in Pb isotopic composition in modern crystalline rocks.

Inter-element fractionation of Pb/U is generally ~5%, whereas apparent fractionation of Pb isotopes is generally <0.2%. In-run analysis of fragments of a large Sri Lanka zircon crystal (generally every fifth measurement) with a known age of 563.5 ± 3.2 Ma (2-sigma error) is used to correct for this fractionation. The uncertainty resulting from the calibration correction is generally 1-2% (2-sigma) for both 206Pb/207Pb and 206Pb/238U ages.

Concentrations of U and Th are calibrated relative to the Sri Lanka zircon, which contains ~518 ppm of U and 68 ppm Th.

The analytical data are reported in Supplemental Text Item #3. Uncertainties shown in the data table are at the 1-sigma level, and include only measurement errors. Analyses that are >30% discordant (by comparison of 206Pb/238U and 206Pb/207Pb ages) or >5% reverse discordant are not considered further.

The resulting interpreted ages are shown on Pb*/U concordia diagrams and relative age-probability diagrams using the routines in Isoplot (Ludwig, 2008). The age-probability diagrams show each age and its uncertainty (for measurement error only) as a normal distribution, and sum all ages from a sample into a single curve.

References:

Gehrels, G.E., Valencia, V., Ruiz, J., 2008, Enhanced precision, accuracy, efficiency, and spatial 	resolution of U-Pb ages by laser ablation–multicollector–inductively coupled plasma–mass 	spectrometry: Geochemistry, Geophysics, Geosystems, v. 9, Q03017, 	doi:10.1029/2007GC001805.

Gehrels, G.E., Valencia, V., Pullen, A., 2006, Detrital zircon geochronology by Laser-Ablation 	Multicollector ICPMS at the Arizona LaserChron Center, in Loszewski, T., and Huff, W., 	eds., Geochronology: Emerging Opportunities, Paleontology Society Short Course: 	Paleontology Society Papers, v. 11, 10 p.

Ludwig, K.R., 2008, Isoplot 3.60.  Berkeley Geochronology Center, Special Publication No. 4, 	77 p.

Stacey, J.S., and Kramers, J.D., 1975, Approximation of terrestrial lead isotope evolution by a 	two‑stage model: Earth and Planetary Science Letters, v. 26, p. 207‑221.