Summary of the Analysis

For 40Ar/39Ar analysis, 1 rock sample was submitted to the Geochronology laboratory at UAF where it was crushed, sieved, washed and hand-picked for phenocryst free rock chips (1000 microns to 500 micron size fraction). The monitor mineral MMhb-1 (Samson and Alexander, 1987) with an age of 523.5 Ma (Renne et al., 1994) was used to monitor neutron flux (and calculate the irradiation parameter, J). The samples and standards were wrapped in aluminum foil and loaded into aluminum cans of 2.5 cm diameter and 6 cm height. The samples were irradiated in position 5c of the uranium enriched research reactor of McMaster University in Hamilton, Ontario, Canada for 20 megawatt-hours.

Upon their return from the reactor, the sample and monitors were loaded into 2 mm diameter holes in a copper tray that was then loaded in a ultra-high vacuum extraction line.  The monitors were fused, and samples heated, using a 6-watt argon-ion laser following the technique described in York et al. (1981), Layer et al. (1987) and Benowitz et al., (2014). Argon purification was achieved using a liquid nitrogen cold trap and a SAES Zr-Al getter at 400C.  The samples were analyzed in a VG-3600 mass spectrometer at the Geophysical Institute, University of Alaska Fairbanks. The argon isotopes measured were corrected for system blank and mass discrimination, as well as calcium, potassium and chlorine interference reactions following procedures outlined in McDougall and Harrison (1999). Typical full-system 8 min laser blank values (in moles) were generally 2 × 10-16 mol 40Ar, 3 × 10218 mol 39Ar, 9 × 10-18 mol 38Ar and 2 × 10-18 mol 36Ar, which are 10–50 times smaller than the sample/standard volume fractions. Correction factors for nucleogenic interferences during irradiation were determined from irradiated CaF2 and K2SO4 as follows: (39Ar/37Ar)Ca = 7.06 × 10-4, (36Ar/37Ar)Ca = 2.79 × 10-4 and (40Ar/39Ar)K =  0.0297. Mass discrimination was monitored by running calibrated air shots. The mass discrimination during these experiments was 1.3% per mass unit. While doing our experiments, calibration measurements were made on a weekly– monthly basis to check for changes in mass discrimination with no significant variation seen during these intervals.

A summary of all the 40Ar/39Ar results is given in Table A1, with all ages quoted to the ± 1 sigma level and calculated using the constants of Renne et al. (2010). The integrated age is the age given by the total gas measured and is equivalent to a potassium-argon (K-Ar) age. The spectrum provides a plateau age if three or more consecutive gas fractions represent at least 50% of the total gas release and are within two standard deviations of each other (Mean Square Weighted Deviation less than 2.5).

Benowitz, J. A., Layer, P. W., & Vanlaningham, S., 2014, Persistent long-term (c. 24 Ma)

exhumation in the Eastern Alaska Range constrained by stacked thermochronology. Geological Society, London, Special Publications, 378(1), 225-243.

Layer, P.W., Hall, C.M. & York, D., 1987, The derivation of 40Ar/39Ar age spectra of single grains of hornblende and biotite by laser step heating, Geophys. Res. Lett., 14, 757-760.

McDougall, I. and Harrison, T.M., 1999, Geochronology and Thermochronology by the 40Ar/39Ar method-2nd ed, Oxford University Press, New York, 269pp.

Renne, P. R., Mundil, R., Balco, G., Min, K., and Ludwig, K. R., 2010. Joint determination of 40K decay constants and 40Ar∗/40K for the Fish Canyon sanidine standard, and improved accuracy for 40Ar/39Ar geochronology.Geochimica et Cosmochimica Acta, 74(18), 5349.

Renne, P. R., Deino, A. L., Walter, R. C., Turrin, B. D., Swisher, C. C., Becker, T. A., Curtis, G.H., Sharp. W.D., and Jaouni, A. R., 1994, Intercalibration of astronomical and radioisotopic time. Geology, 22(9), 783-786.

Samson S. D., and Alexander E. C. (1987) Calibration of the interlaboratory 40Ar/39Ar dating standard, MMhb1. Chem. Geol. 66, 27-34.

Steiger, R.H. and Jaeger, E., 1977, Subcommission on geochronology: Convention on the use of decay constants in geo and cosmochronology, Earth and Planet Science Letters, v. 36, p. 359-362.

York, D., Hall, C.M., Yanase, Y., Hanes, J.A. & Kenyon, W.J., 1981. 40Ar/39Ar dating of terrestrial minerals with a continuous laser, Geophys. Res. Lett., 8, 1136-1138.

Supplemental Table A1 Interpretive Details

| Sample | Min. | Integrated Age (Ma) | Plateau Age (Ma) | Plateau Information | Isochron Age (Ma) | Isoochron or other Information |
| --- | --- | --- | --- | --- | --- | --- |
| 14JR21 | WR | 51.7 ± 0.7 | 52.0 ± 0.9 | 7 of 11 fractions 63.6% 39Ar release MSWD = 1.15 | 49.1 ± 1.6 | 7 of 11 fractions 40Ar/36Ari = 301.9 ± 4.2 MSWD = 0.66 |

Samples analyzed with standard MMhb-1 an age of 523.5 Ma.

Most robust age in bold.

Supplemental Figure Captions:

Supplemental Figure A1:  40Ar/39Ar age spectra, Ca/K and Cl/K ratios for sample from 14JR21. Steps filled in grey were used for plateau age determinations. Steps filled in red were used for age determination.

Supplement Table A1: 40Ar/39Ar step heating results.

Supplemental Table A2: 40Ar/39Ar laser step heat data.

| Supplemental Table A2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Laser=L |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 14JR21 WR#L1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Weighted average of J from standards = 3.107e-03 +/- 8.884e-06 |  |  |  |  |  |  |  |  |  |  |  |  |
| Laser Power | Cumulative | 40Ar/39Ar | +/- | 37Ar/39Ar | +/- | 36Ar/39Ar | +/- | % Atm. | +/- | Ca/K | +/- | Cl/K | +/- | 40*/39K | +/- | Age | +/- |
| (mW) | 39Ar | meas. |  | meas. |  | meas. |  | 40Ar |  |  |  |  |  |  |  | (Ma) | (Ma) |
| 250 | 0.0037 | 1124.6004 | 24 | 2.19638 | 0.0733 | 3.72437 | 0.0904 | 97.84801 | 1.1583 | 4.03632 | 0.1348 | 0.02062 | 0.00384 | 24.23828 | 13.0627 | 130.82 | 68.01 |
| 500 | 0.0237 | 302.57237 | 1.611 | 1.98579 | 0.0133 | 0.97405 | 0.0083 | 95.08335 | 0.6814 | 3.64877 | 0.0245 | 0.0111 | 0.00076 | 14.89585 | 2.07406 | 81.52 | 11.1 |
| 750 | 0.0956 | 78.45641 | 0.293 | 1.88758 | 0.0129 | 0.2297 | 0.0018 | 86.34998 | 0.6103 | 3.46807 | 0.0238 | 0.00958 | 0.00027 | 10.71956 | 0.48447 | 59.03 | 2.62 |
| 1000 | 0.195 | 38.08447 | 0.146 | 2.90685 | 0.014 | 0.0982 | 0.0015 | 75.62269 | 1.1183 | 5.34464 | 0.0259 | 0.00421 | 0.00027 | 9.29583 | 0.42976 | 51.3 | 2.34 |
| 1500 | 0.3091 | 40.59898 | 0.12 | 5.65294 | 0.0196 | 0.1068 | 0.0012 | 76.64383 | 0.864 | 10.41394 | 0.0362 | 0.00491 | 0.00013 | 9.51344 | 0.35448 | 52.49 | 1.93 |
| 2000 | 0.4435 | 32.06499 | 0.111 | 5.93458 | 0.0236 | 0.0788 | 0.0009 | 71.1566 | 0.7967 | 10.93497 | 0.0437 | 0.00331 | 0.00013 | 9.27899 | 0.26023 | 51.21 | 1.42 |
| 2250 | 0.5044 | 22.9289 | 0.102 | 9.66775 | 0.0423 | 0.04804 | 0.0017 | 58.51401 | 2.2174 | 17.86094 | 0.0787 | 0.00605 | 0.0002 | 9.56535 | 0.51345 | 52.77 | 2.79 |
| 2500 | 0.5415 | 32.04265 | 0.145 | 11.44379 | 0.0583 | 0.07707 | 0.0028 | 68.19771 | 2.5899 | 21.16887 | 0.1086 | 0.01316 | 0.00044 | 10.26388 | 0.83761 | 56.56 | 4.54 |
| 3000 | 0.5785 | 39.48947 | 0.205 | 13.5876 | 0.0711 | 0.10217 | 0.0029 | 73.67137 | 2.1563 | 25.17292 | 0.1331 | 0.0278 | 0.00057 | 10.48995 | 0.86182 | 57.79 | 4.67 |
| 5000 | 0.7326 | 17.03606 | 0.052 | 9.26296 | 0.0266 | 0.0298 | 0.0007 | 47.28101 | 1.1632 | 17.10818 | 0.0494 | 0.05804 | 0.00036 | 9.02472 | 0.20168 | 49.83 | 1.1 |
| 9000 | 1 | 11.52747 | 0.021 | 16.95793 | 0.0323 | 0.01588 | 0.0005 | 28.64544 | 1.2712 | 31.49262 | 0.0607 | 0.04128 | 0.0002 | 8.30389 | 0.14894 | 45.9 | 0.81 |
| Integrated |  | 38.21907 | 0.042 | 9.41417 | 0.0109 | 0.10034 | 0.0004 | 75.60813 | 0.3204 | 17.38932 | 0.0202 | 0.02428 | 0.00009 | 9.37749 | 0.12425 | 51.75 | 0.69 |